## Slide 1: 5G NTN and 6G Satellite Link Design
Sassan Ahmadi
Murthy Upmaka
Keysight Technologies

## Slide 2
You will learn:
Overview of NTN
Challenges in designing an NTN link
The methodology to design an NTN link
SystemVue software that helps designing the NTN link
A case study of a link budget analysis
5G NTN and 6G Satellite Link Design

## Slide 3: 5G/6G NTN Technologies
Agenda
Overview of NTN and use cases
5G/6G NTN technologies and vendor/operator challenges
3GPP NTN roadmap and 6G NTN outlook
NTN architectures and characteristics
NTN link budget analysis
System design challenges and solutions
A case study
Summary

## Slide 4: 5G/6G NTN Technologies
NTN: Non-Terrestrial Network
enhancing connectivity and transforming current capabilities
The Definitive Guide to Non-Terrestrial Networks - ebook
Ubiquitous Service
Notes: The space and satellite industry is experiencing rapid evolution driven by new companies, research efforts, and investment.
80% population has wireless access
40% of the globe has wireless coverage
Although we think primarily of satellites in NTNs, other components can consist of low-altitude platforms / drones (LAP), high-altitude pseudo satellites / drones / balloons (HAPS), satellites across the various orbits, and combinations of these.
GEO: geosynchronous equatorial orbit
MEO:medium Earth orbit
LEO:low Earth orbit

## Slide 5: Satellite Orbits

## Slide 6: 5G/6G NTN Technologies: use cases
NTN: Non-Terrestrial Network
Urban : helps offloading, network resiliency, fixed wireless, emergency
Rural : Fixed wireless, network resiliency, emergency, Public protection and disaster relief
Remote: Network resiliency, PPDR, emergency, backhaul, wide area connectivity
Isolated: Aeronautical, Maritime, PPDR and emergency
Mainly to augment the TN (terrestrial network)
Notes: The space and satellite industry is experiencing rapid evolution driven by new companies, research efforts, and investment.
80% population has wireless access
40% of the globe has wireless coverage
Although we think primarily of satellites in NTNs, other components can consist of low-altitude platforms / drones (LAP), high-altitude pseudo satellites / drones / balloons (HAPS), satellites across the various orbits, and combinations of these.
GEO: geosynchronous equatorial orbit
MEO:medium Earth orbit
LEO:low Earth orbit

## Slide 7: 5G/6G NTN Technologies: use case examples
NTN: Non-Terrestrial Network
Each use case might require a different technology.
Examples:
1. Continuous communication, high data rates such as satellite internet
Huge dish communicating to GEO satellite
2. Hand phone in a remote area sending an SOS signal to satellite.
Lower Path Loss requiring communicating with LEO satellite
3. In a stadium 10s of thousands communicating
Set up a drone-based network
Notes: The space and satellite industry is experiencing rapid evolution driven by new companies, research efforts, and investment.
80% population has wireless access
40% of the globe has wireless coverage
Although we think primarily of satellites in NTNs, other components can consist of low-altitude platforms / drones (LAP), high-altitude pseudo satellites / drones / balloons (HAPS), satellites across the various orbits, and combinations of these.
GEO: geosynchronous equatorial orbit
MEO:medium Earth orbit
LEO:low Earth orbit

## Slide 8: 5G/6G NTN Technologies: use case examples
NTN: Non-Terrestrial Network
GEO satellite : Higher path loss and large delay. Higher cost of satellite deployment
LEO satellite : Path loss, moderate delay, doppler, requiring handoff for continuous comms
drone-based network: Higher multipath fading, interference
We need to design the links with different technologies to meet the challenges
Notes: The space and satellite industry is experiencing rapid evolution driven by new companies, research efforts, and investment.
80% population has wireless access
40% of the globe has wireless coverage
Although we think primarily of satellites in NTNs, other components can consist of low-altitude platforms / drones (LAP), high-altitude pseudo satellites / drones / balloons (HAPS), satellites across the various orbits, and combinations of these.
GEO: geosynchronous equatorial orbit
MEO:medium Earth orbit
LEO:low Earth orbit

## Slide 9: 5G/6G NTN Technologies
Overview of NTN and use cases
5G/6G NTN technologies and vendor/operator challenges
3GPP NTN roadmap and 6G NTN outlook
NTN architectures and characteristics
NTN link budget analysis
System design challenges and solutions
A case study
Summary
Agenda:

## Slide 10: 5G/6G NTN Technologies: Customer Challenges
NTN started in Rel-17 and continues to evolve in Rel -18 and 19 in 5G advanced
Marching to be integral part of 6G
The main considerations are
Selection of the best NTN technologies
Modeling RF and propagation channel realistically
Optimize the TN with minimum impact from NTN
Create digital twins that give a clear idea of ROI

## Slide 11: 5G/6G NTN Technologies
Overview of NTN and use cases
5G/6G NTN technologies and vendor/operator challenges
3GPP NTN roadmap and 6G NTN outlook
NTN architectures and characteristics
NTN link budget analysis
System design challenges and solutions
A case study
Summary
Agenda:

## Slide 12: 3GPP NTN Roadmap
Source: 3GPP and “The path to 5G-Advanced and 6G Non-Terrestrial Network systems” by Alessandro Guidotti et al.

## Slide 13: 6G NTN: Integrated Non-Terrestrial Networks
Seamless NTN-TN Integration: Requires thorough interference modeling and spectrum sharing strategies.
Advanced Antenna and RF Design: Large antenna arrays, beamforming, and energy-efficient RF circuitry are essential in the gateway, satellite and the terminals.
Digital Twin and Realistic Modeling: Critical for design, testing, and adoption of NTN technologies.
Optical vs. Microwave Inter-Satellite Links: Requires careful interference and performance analysis.
Testing & Verification Methodologies: Fundamental to ensure trust, reliability, and deployment feasibility.
NTN Gateway with Parabolic or Phased-Array Antenna (RU)
Transparent/Regenerative NTN Payload with Phased-Array Antenna
(DU + RU) or RU
UE
UE
UE
Transparent/Regenerative NTN Payload with Phased-Array Antenna
(DU + RU) or RU
Optical/mmWave Links
Edge Cloud (CU)
Core Cloud (5GC/vEPC)
[UE to UE via Satellite]
Source:2022 11th Advanced Satellite Multimedia Systems Conference and the 17th Signal Processing for Space Communications Workshop (ASMS/SPSC)
3GPP and “The path to 5G-Advanced and 6G Non-Terrestrial Network systems” by Alessandro Guidotti et al.

## Slide 14: 5G/6G NTN Technologies
Overview of NTN and use cases
5G/6G NTN technologies and vendor/operator challenges
3GPP NTN roadmap and 6G NTN outlook
NTN architectures and characteristics
NTN link budget analysis
System design challenges and solutions
A case study
Summary
Agenda:

## Slide 15: Modeling Non-Terrestrial Networks
Large-scale Fading Effects: LOS probability, Path loss and shadow fading, O2I penetration loss, atmospheric absorption (above 10GHz), rain and cloud attenuation (above 6 GHz), Ionospheric (below 10GHz) and Tropospheric (above10GHz) scintillation, Faraday [polarization] rotation (3dB polarization loss)
Small-scale Fading Effects: Flat and frequency-selective fading, Coherence [Time/Bandwidth/Distance] vs [Doppler/Delay/Angle] spread
NTN experiences higher carrier frequency offset (CFO) and sampling time offset (STO) effects, Doppler shift due to satellite movement depends on the satellite orbit, elevation angle, and carrier frequency, PA nonlinearity, co-channel/adjacent channel interference, I/Q imbalance, link budget, antenna arrays, beamforming, noise and distortion, impedance mismatch, intermodulation and harmonic distortion, etc.

## Slide 16: 5G/6G NTN Frequency Bands
NR Operating Band | Uplink | Downlink | Bandwidth (MHz) | Duplex Mode
n253 | 1668 MHz – 1675 MHz | 1518 MHz –1525 MHz | 5,10,15,20,30 | FDD
n254 | 1610 MHz – 1626.5 MHz | 2483.5 MHz – 2500 MHz | 5,10,15,20,30 | FDD
n255 | 1626.5 MHz – 1660.5 MHz | 1525 MHz – 1559 MHz | 5,10,15,20,30 | FDD
n256 | 1980 MHz – 2010 MHz | 2170 MHz – 2200 MHz | 5,10,15,20,30 | FDD
n510 | 27.5 GHz – 28.35 GHz | 17.7 GHz – 20.2 GHz | 50,100,200,400 | FDD
n511 | 28.35 GHz – 30.0 GHz | 17.7 GHz – 20.2 GHz | 50,100,200,400 | FDD
n512 | 27.5 GHz – 30.0 GHz | 17.7 GHz – 20.2 GHz | 50,100,200,400 | FDD
n23 | 2000 MHz – 2020 MHz | 2180 MHz – 2200 MHz |  | FDD
5G NTN and NTN IoT Band Considerations
Low-power IoT devices require L/S-band for extended coverage and battery life.
High-data rate applications (e.g., VSATs, cell phones) may use Ku/Ka-band for faster and wider bandwidth transmission.
Regulatory & standardization efforts (e.g., 3GPP Rel-17 & Rel-18) are defining NTN IoT spectrum allocation.

## Slide 17: 5G/6G NTN Technologies
Overview of NTN and use cases
5G/6G NTN technologies and vendor/operator challenges
3GPP NTN roadmap and 6G NTN outlook
NTN architectures and characteristics
NTN link budget analysis
System design challenges and solutions
A case study
Summary
Agenda:

## Slide 18: Link Budget Analysis
Background Information
The Reference Sensitivity is a range of values that can be calculated as where is the thermal noise power in dBm, is the noise equivalent bandwidth, is the maximum receiver noise figure, is the minimum SINR for the chosen MCS, is the implementation margin.
The noise floor for any receiver is defined as , where (in dB) is a measure of SINR degradation by the components in the RF signal path including the RF filters and low-noise amplifier. The thermal noise power density is measured at typical room temperature.
Signal Power
Noise Power
Interference Power

## Slide 19: Link Budget Analysis
Background Information
Link budget shows how different components and propagation processes influence the available SNR at the receiver. It can be used to compute the required transmit power, dynamic range of a system, or the required receiver sensitivity.
Link budget is a commonly used metric to evaluate the coverage of a cellular system in the downlink or uplink.
EIRP is Effective Isotropic Radiated Power. The EIRP can be related to the transmit power (PTX), the cable losses (and possibly including antenna mismatch) L, and the antenna gain (G) by
EIRP=PTX-L+G
Free Space Path Loss

## Slide 20: 5G NTN-IoT Link Budget Analysis (Example)
Set Satellite Payload Characteristics
Set UE Payload Characteristics
Set Link Characteristics
Set NB-IoT Channel Parameters
From effective coding rate Compute Reference CNR
Compute Link Budget
Compute Link Margin and NB-IoT Repetitions
Link budget analysis is an essential step in the design of radio and satellite communication systems for calculating the performance of the system and type of services offered by the system by accounting for power gains and losses across the transmission and propagation paths.

## Slide 21: NTN-IoT Link Budget Analysis (Example)
Satellite orbit |  | GEO | LEO-1200 | LEO-600
Satellite altitude |  | 35786 km | 1200 km | 600 km
Payload characteristics for DL transmissions |  |  |  | 
Equivalent Satellite Antenna Aperture | S-band (i.e. 2 GHz) | 22 m | 2 m | 2 m
Satellite EIRP Density |  | 59 dBW/MHz | 40 dBW/MHz | 34 dBW/MHz
Satellite Tx Max Gain |  | 51 dBi | 30 dBi | 30 dBi
3db Beamwidth |  | 0.4011 deg | 4.4127 deg | 4.4127 deg
Satellite Beam Diameter |  | 250 km | 90 km | 50 km
Equivalent Satellite Antenna Aperture | Ka-band (i.e. 20 GHz for DL) | 5 m | 0.5 m | 0.5 m
Satellite EIRP Density |  | 40 dBW/MHz | 10 dBW/MHz | 4 dBW/MHz
Satellite Tx Max Gain |  | 58.5 dBi | 38.5 dBi | 38.5 dBi
3db Beamwidth |  | 0.1765 deg | 1.7647 deg | 1.7647 deg
Satellite Beam Diameter |  | 110 km | 40 km | 20 km
Payload Characteristics For UL Transmissions |  |  |  | 
Equivalent Satellite Antenna Aperture | S-band (i.e. 2 GHz) | 22 m | 2 m | 2 m
G/T |  | 19 dB K-1 | 1.1 dB K-1 | 1.1 dB K-1
Satellite Rx Max Gain |  | 51 dBi | 30 dBi | 30 dBi
Equivalent Satellite Antenna Aperture | Ka-band (i.e. 30 GHz for UL) | 3.33 m | 0.33 m | 0.33 m
G/T |  | 28 dB K-1 | 13 dB K-1 | 13 dB K-1
Satellite Rx Max Gain |  | 58.5 dBi | 38.5 dBi | 38.5 dBi
Parameters | Values
Carrier Frequency | 2 GHz for DL and UL (S-band)
System Bandwidth | 30 MHz (S-band), 400 MHz (Ka-band)
Channel Bandwidth | Downlink: 180 kHz Uplink: 3.75, 15, 45, 90, or 180 kHz
Satellite Altitude | 35786 km (GEO)
Target Elevation Angle | 10.95, 20°
Atmospheric Loss | 0.2 dB
Shadowing Margin | 3 dB
Scintillation Loss | Ionospheric loss: = 2.2 dB Tropospheric loss: ITU-R P618
Additional Loss | 0 dB
Frequency Reuse Factor | 1, 2, 3
Satellite Antenna Polarization | Circular polarization
Terminal Type | Ka-band: VSAT S band: (M, N, P) = (1,1,2)
Free Space Path Loss | 
Terminal RF Parameters | Tx Power = 23 dBm, Tx/Rx Antenna Gain = 0 dBi, Rx Noise Figure = 7 dB Rx Antenna Temperature = 290o K
Polarization Loss | 3 dB

## Slide 22: NTN-IoT Link Budget Analysis Metrics
Calculate Required CNR for the Selected MCS
Calculate Effective Code Rate
Calculate Receiver (GW,SAT,UE) Antenna G/T
Calculate the Actual CNR
Calculate Link Margin
Calculate the Number of Repetitions to Achieve the Required CNR

## Slide 23: 5G/6G NTN Technologies
Overview of NTN and use cases
5G/6G NTN technologies and vendor/operator challenges
3GPP NTN roadmap and 6G NTN outlook
NTN architectures and characteristics
NTN link budget analysis
System design challenges and solutions
A case study
Summary
Agenda:

## Slide 24
Gateway Baseband Signal Processing
Gateway TX RF Processing
UE Baseband Signal Processing
UE RX RF Processing
NB-IoT Signal Parameters
I/Q LPF  Mixer  BPF  VGA/PA  TX BPF  Circulator  Ant
Parameters
TX Antenna Parameters
Gain, EIRP, Beam Misalignment, Output Power, Efficiency, etc.
RX Antenna Parameters
Gain, RX G/T, Efficiency, etc.
Circulator  RX BPF  LNA  Mixer  I/Q LPF
Feeder Link Propagation Parameters and Losses
Service Link Propagation Parameters and Losses
Payload RF Processing at F1
Payload RF Processing at F2
Payload RX Antenna Parameters
Gain, RX G/T, Efficiency, etc.
Payload TX Antenna Parameters
Gain, EIRP, Beam Misalignment, Output Power, Efficiency, etc.
NB-IoT Signal Parameters + SINR, Repetition, etc.
5G/6G NTN Technologies: System Challenges
Create a standard based waveform
Model noise, non-linearities, mismatch, frequency response, temp response etc.
Real antenna pattern, matching with FE electronics, misalignmen tloss
Model noise, non-linearities, mismatch, frequency response, temp response etc.
Model noise, non-linearities, mismatch, frequency response, temp response etc.
Model all types of losses, doppler and delay
Size, weight, power, beam steering, misalignment loss
Size, weight, power, beam steering, misalignment loss
Dynamics of satellite motion
Base band impairments, signal processing

## Slide 25
Need to integrate across physical, numerical, time and frequency domains.
We need sophisticated tools
5G/6G NTN Technologies: System Challenges – the solutions

## Slide 26: SystemVue at a Glance
Channel
Model / Fading
Transmitter
Model
Signal, BB & RF
Receiver
Model
Antenna Array
Antenna Array
Tx
Multi-dimensional accurate RF part modeling
Frequency domain RF line up analysis
Phased array antenna design
5G waveform generation
NTN channel modeling
5G base band receiver
End-to-end simulation of BER/FER/Throughput
Spectrasys
Phased Array Analysis
Signal processing

## Slide 27: SystemVue in your workflow
Channel
Model / Fading
Transmitter
Model
Signal, BB & RF
Receiver
Model
Antenna Array
Antenna Array
RF/µW Circuits and Layout
System-level Performance
Rx Power, EVM,
IMD, ACPR
PAPR, etc.
PNA-X
Measured
X and S
Parameters
Antennas
Keysight Sources, Analyzers, Software
Atmospheric, Terrain, Doppler, Delay, Orbit
PropSim Channel
Emulator
5G NTN
EXata
C++
HDL Python
EIRP
Tx

## Slide 28: 5G/6G NTN Technologies
Overview of NTN and use cases
5G/6G NTN technologies and vendor/operator challenges
3GPP NTN roadmap and 6G NTN outlook
NTN architectures and characteristics
NTN link budget analysis
System design challenges and solutions
A case study
Summary
Agenda:

## Slide 29
Gateway Baseband Signal Processing
Gateway TX RF Processing
UE Baseband Signal Processing
UE RX RF Processing
Payload RF Processing at F1
Payload RF Processing at F2
Case Study – NTN link budget analysis
Feeder
Channel
Service
Channel

## Slide 30
5G/6G NTN Technologies: System design
Allows modeling of Satellite link
Animation for to visualize scenario
Models various loss mechanisms
  Pathloss
  Scintillation
  Polarization
  Faraday rotation
  Shadowing etc.
Computes doppler
Computes delay

## Slide 31
5G/6G NTN Technologies: System design

## Slide 32
5G/6G NTN Technologies: System design - frequency domain
Tx
Bent Pipe
Rx
Antennas
Channel
Feeder
Service
Integrate RF subsystems, Antennas and channel accurately and simulate quickly

## Slide 33
Gateway Tx
Bent Pipe
UE Rx
5G/6G NTN Technologies: System design – frequency domain

## Slide 34
5G/6G NTN Technologies: System design – frequency domain
Integrate RF subsystems, Antennas and channel accurately and simulate quickly
Simulates in seconds!

## Slide 35
5G/6G NTN Technologies: System design

## Slide 36
5G/6G NTN Technologies: System design – time domain

## Slide 37
5G/6G NTN Technologies: System design

## Slide 38
5G/6G NTN Technologies: System design
It is fast and accurate, agreed.
What about user experience and integrating into a workflow?
User definable GUI 

## Slide 39: 5G/6G NTN Technologies
Overview of NTN and use cases
5G/6G NTN technologies and vendor/operator challenges
3GPP NTN roadmap and 6G NTN outlook
NTN architectures and characteristics
NTN link budget analysis
System design challenges and solutions
A case study
Summary
Agenda:

## Slide 40: Summary
Simulating an end-to-end NTN transmission path
NTN link budget analysis is hard
Keysight’s SystemVue is a comprehensive tool perform NTN link budget analysis
SystemVue is conducive to be integrated into diverse workflows.
NTN is here to stay and progressing to be an integral part of 6G.

## Slide 41: Learn More
Keysight W4516E PathWave 5G NR NTN Channel Model Kit
Keysight W4503E PathWave Phased Array Simulation
Keysight W4540E PathWave DPD Explorer in PathWave ADS | Keysight
Keysight W4522E PathWave 5G And Cellular Library

## Slide 42: Resources
Website: SystemVue: System-level Design and Simulation Software
W4804B SystemVue Core, RF, Comms/DSP, Phased Array Bundle
SystemVue Bundles

## Slide 44: Back up slides

## Slide 45: 5G Non-Terrestrial Networks Use Cases
Satellite communication [broadcast satellite services (BSS), fixed satellite services (FSS), and mobile satellite services (MSS)] has existed for a few decades; however, new 3GPP standards are meant to complement and integrate space coverage with terrestrial networks.
Source: Rohde & Schwarz

## Slide 46: Downlink Scenario: LEO Satellite at 600 km Altitude
Feeder Link
(Proprietary Link for TTC and 3GPP LTE/NR for NTN Typically using Ka band)
Service Link
Specified by 3GPP (LTE/NR)
Ground Station (NTN Gateway) with Parabolic Antenna or Phased-Array Antenna
UE or IoT Device
NB-IoT Downlink Signal Generation and RF Processing
NB-IoT Downlink Signal Reception and RF Processing
See Table 6.2-4 of TR 36.763 for the payload transmission parameters
See Table 6.2-1and 6.2-2 of TR 36.763 for propagation parameters (LEO 600 km)
UE power class (PC5=20 dBm)
- UE Noise Figure (NF=9 dB)
Channel Bandwidth for NB-IoT: NB-IoT 180 kHz (DL), Up to 180 kHz with all permissible smaller resource allocations 12*15 kHz, 6*15 kHz, 3*15 kHz, 1*15 kHz, 1*3.75 kHz (UL)
UL/DL Frequency: Band 254 (see Table 5.1.1-1 of TR 36.764
Reference sensitivity for UE category NB1 and NB2: -108.2dBm (see TR 36.784 Table 6.2.2.1-4)
NTN Payload with Phased-Array Antenna
 | Uplink Antenna |  |  |  | Downlink Antenna |  |  | 
Satellite | SpaceX | Telesat | OneWeb | Amazon | SpaceX | Telesat | OneWeb | Amazon
Diameter (m) | 1.5 | 1.5 | 3.5 | 2.4 | 1.5 | 1.5 | 3.5 | 2.4
Above ground level (m) | 1.95 | 3.2 | 4.55 | - | 1.95 | 3.2 | 4.55 | -
EIRP (dBW) | 68.4 | 75.9 | 63.2 | 62.3 | 39.44 | 38 | 30.6–39 | 36
Max Gain (dBi) | 41 | 31.8 | - | 53.1 | 46.9 | 45.5 | 51.5 | 50.2
Elevation (deg) | 25 | 10 | 15 | 20 | 25 | 10 | 15 | 20
Path distance (km) | 2439 | 1504 | 1684 | 590 | 2439 | 1504 | 1684 | 590
SV Gateway Model:
https://pmc.ncbi.nlm.nih.gov/articles/PMC9740709/

## Slide 47: Uplink Scenario: LEO Satellite at 600 km Altitude
Service Link
Specified by 3GPP
Ground Station with Directive Parabolic Antenna or Phased-Array
UE or IoT Device
NB-IoT Uplink Signal Reception and RF Processing
NB-IoT Uplink Signal Generation and RF Processing
See Tables 6.1 and 6.2-2 of TR 36.763 for transmission parameters
See Table 6.2-1of TR 36.763 for propagation parameters
UE power class (PC5=20 dBm)
- UE Noise Figure (NF=9 dB)
Channel Bandwidth for NB-IoT: NB-IoT 180 kHz (DL), Up to 180 kHz with all permissible smaller resource allocations 12*15 kHz, 6*15 kHz, 3*15 kHz, 1*15 kHz, 1*3.75 kHz (UL)
UL/DL Frequency: Band 253 (see Table 5.1.1-1 of TR 36.764
Feeder Link
(Proprietary Link for TTC and 3GPP LTE/NR for NTN Typically using Ka band)
 | Uplink Antenna |  |  |  | Downlink Antenna |  |  | 
Satellite | SpaceX | Telesat | OneWeb | Amazon | SpaceX | Telesat | OneWeb | Amazon
Diameter (m) | 1.5 | 1.5 | 3.5 | 2.4 | 1.5 | 1.5 | 3.5 | 2.4
Above ground level (m) | 1.95 | 3.2 | 4.55 | - | 1.95 | 3.2 | 4.55 | -
EIRP (dBW) | 68.4 | 75.9 | 63.2 | 62.3 | 39.44 | 38 | 30.6–39 | 36
Max Gain (dBi) | 41 | 31.8 | - | 53.1 | 46.9 | 45.5 | 51.5 | 50.2
Elevation (deg) | 25 | 10 | 15 | 20 | 25 | 10 | 15 | 20
Path distance (km) | 2439 | 1504 | 1684 | 590 | 2439 | 1504 | 1684 | 590
SV Gateway Model:
https://pmc.ncbi.nlm.nih.gov/articles/PMC9740709/

## Slide 48: Starlink Example Non-3GPP Compliant Service Link

## Slide 49: SystemVue Value Proposition for 6G
SystemVue provides
  An intuitive software tool for system-level modeling with exceptional accuracy and fidelity.
  Customizable levels of realism for system components and impairments, ensuring precise simulations.
It can help users to develop accurate system-level Digital Twins of 5G/6G NTN technologies; simulate and benchmark performance using realistic baseband, RF and antenna models.
  Users can
    Generate the Desired Waveforms (e.g., 4G LTE/5G NR, NB-IoT, and more)
    Process the Waveforms through Realistic RF Transceiver and Antenna Models
    Generate AI/ML Model Training Data with SystemVue and Use Trained Model Parameters in SystemVue to Assess the Performance Gains
    Derive Real-World Device Models and Use their Parameters in SystemVue
    Use Realistic Propagation and Channel Models (e.g., 3D and Ray Tracing, and more)

## Slide 50: Non-Terrestrial Networks Modeling
Gateway, Payload and UE Antenna Array Modeling
PA and DPD Performance Modeling
Nonlinearity Modeling