## Slide 1: Re-imagining RF Design Using ADS Python APIs & AI/ML
Daren McClearnon
AI/ML Prod Mgr, Keysight EDA
07 March 2025

## Slide 2: Re-imagining RF Design Using ADS Python APIs & AI/ML
Agenda
Python APIs in ADS
Case 1: Generative AI for Loadpull (Video from Baylor Univ)
Case 2: “QR Code” Filters with RFPro (Video from Chalmers Univ)
AI/ML Technologies in ADS
Objectives of this module
Awareness of ADS Python APIs, emerging applications
Learn how people are putting Data into motion using Automation and AI/ML
See resources to help you get started

## Slide 3: Customer/Industry Challenges
EDA Industry & Customer Challenges
Shorter market windows, greater complexity
Complex tool flows
Skilled Engineers are at a premium
Scalable, but…
    ….needs to be secure, traceable, sustainable
Buildings
Factories
Equipment
Information??
Automation
Enables information to become more like a tangible asset
Engineering organizations who fully leverage information assets will be more successful than those who do not or cannot.
 Put Your Data in Motion
Notes: -----
EDA Industry & Customer Challenges
Shorter market windows, greater complexity
Complex tool flows
  Across multiple vendors, formats, workflows.
  increase design costs, skill requirements
  create islands that slow down workflows, cross-validation
  create single-vendor risks
Skilled Engineers are at a premium
  talent shortage
Scalable, but…
  ….needs to be secure, traceable, sustainable
------
Keysight EDA Challenges
Accelerating Change
  EDA industry, Technology, Design Methods, AI
Complex Platforms, Workflows, Tools
  Large, “mature”, monolithic platform
  Rigid integration, specialized skills
  Long learning curve
  DevSecOps, Export complexity
Disjointed product islands
  IP, Data, Formats, APIs
Enterprise Scalability
  Licensing, Security, Business models
  Cloud and HPC deployment models
  Operational and Workflow integration

## Slide 4: Keysight Solution Approach – Move Toward An Application Layer
Electronic product lifecycles and workflows usually span many functional boundaries
Development of an Application Layer
  Efficiency: Streamlined Design personalities
  Agility: react quickly to changing opportunities
  Innovation: keep pace at the speed of the industry, create proprietary advantages
Scalability
  Connect to HPC, parallelization, GPU accel
  Enterprise system integration
  Unlock potential for AI/ML and machine-driven automation
API / Automation
AI / ML
IP & Data
Management
Keysight EDA tools
API / Automation
AI / ML
IP & Data
Management
Other EDA Tools
Other EDA Tools
Keysight EDA tools

## Slide 5: Keysight Solution Approach – Modularity and APIs
Create tailored, more efficient Workflows, Personas, and Use Cases, while enabling a future “Agentic” Layer
Overcoming Rigid, Complex Tools
    More Modularity, APIs, SDKs/Toolkits
    Move from “Tasks”  “Workflows”
Adapt faster with intelligent Automation and accelerate Value Generation
Cross traditional boundaries between functional blocks and vendors
Enable New Use Cases
Quickly address opportunities
Keysight EDA Apps, Services
Customer Self-integrated Apps
3rd Party & Research Partner Apps
Nexus
Circuit Sim
RFPro
EM
Schematic
Layout
Data
Data
Display
ETH
System
HPC
PDK
Plug-ins
PW Data Tools
EDA Toolbox
PyTorch
TensorFlow
API Layer
API Docs, Examples
Python IDE’s
ADS has improved its internal Modularity
Python is the popular language choice
Documented APIs make integrations easy

## Slide 6: Broad Python tool support for ADS 2025 U2
EDA Toolbox: “Wrapper API’s” to drive & connect tools
  Simulate a circuit using Python (ADS)
  Co-optimize antenna+ matching network (ADS+ EM Pro)
  Driving SystemVue using Python API (SV)
  Measurement demo (VSA)
PW Data Tools: Data Interoperability
  Universal Data Structures + Easy and Consistent File I/O
  ADS, SV, HFSS, IC-Cap, Touchstone, Citi, Load Pull + more!
data structure
ADS Python Console: ADS Main window, Data Display
Standard IDE’s: Code, Debug, Run with ADS

## Slide 7: Use Cases for Python Automation
Users have Different Motivations and Use Models
Direct link

## Slide 8: Use Case 1 (Productivity) : Measured load pull data importer
LOADPULL DATA IMPORT
Custom Python GUI to import and combine measured data, generating datasets, data displays, testbenches and models.
Datasets and Data Displays
Artificial Neural Network Simulation Models and testbenches
Watch now:
https://www.keysight.com/content/dam/keysight/en/vid/ungate/demos/Load-Pull-Modeling-with-Python-s-AI-Power.mp4
UNFORMATTED
RAW
MEASUREMENTS

## Slide 9: Use Case 1 (Productivity) : Scripted design personalities
Filters created and optimized in a headless, automated method in Keysight ADS – an on-ramp to AI/ML
Guided Flows
can speed up
routine
processes

## Slide 10: Personal Productivity Demo: ADS Filter Workflow
3 ways to run interactive applications
Custom Menu and User Interface
Interactive Jupyter Notebook
ADS Jupyter Python Console
Keysight EDA Connect 2025
KC article
https://docs.keysight.com/display/eesofkcads/ADS+Python+Console+Workflow+Automation+Demo+Stepped+Z+Filter+Synthesis+Setup+Simulate+Optimize+Report

## Slide 11: Use Case 1 (Productivity) : Embedding an Interactive in Data Display
Python callbacks allow QT objects (widgets, lists, buttons, forms) to insert into Data Display Pages
Callback is invoked from a Right Click menu, but you can control that
This code was implemented using the new Python Add on capability in Data Display, where you can add or modify Menus and even pop up a UI
This example ships with ADS 2025, under: $HPEESOF_DIR/dds/python/app/ examples/ex_addon_3d_plot
Note: Beta Feature
Keysight EDA Connect 2025

## Slide 12: Use Case 1 (Productivity): Small customizations
ADS 2025 Update 1 Python: Automate / Customize ADS using native API’s
Create workspace, libraries,
schematics, layouts, symbols
Modify & Edit Existing Designs,
Set or change instance parameters
Work with Vars + MeasEqns
Create Custom Menus, Add-Ons, GUIs
Run inside ADS, or external “headless"
Python console
Jupyter
Notebook
de.create_workspace(path)
de.create_new_library(name,path)
db_uu.create_schematic(LCVname)
db_uu.create_layout(LCVname)
dsn.add_var_instance((x,y), name)
dsn.add_instance(LCVme,(x,y),name,ang)
C1["C"].value=“1.0 pF"
Extract Advanced ANN Models
ann.extract_model(“in.txt","out")
Create + Modify Substrates
Create + Modify Data Displays
menu_bar.add_menu(my_menu)
sub=subst.create_substrate(lib,name)
material=subst.materials[ix]
plot=page.add_plot()
»traces=plot.add_traces(list[str])

## Slide 13: Use Case 2 (Enterprise) : Automated Workflows (digital transformation)
Mobile Handset
Accelerate a Mobile Handset D&V workflow using ADS automation
Time per RF Path | RFPro EM, with setup | Matching Design | Bill of Materials
Traditional workflow (manual) | 60 mins | 40 mins | 20 mins
Automated workflow | 5 mins | 10 mins | 10 secs
Solution approach | Python for manual steps to import & prep for RFPro | Faster optimization with better initial constraints 1-button replace ideal  vendor parts | 1-button BOM generation
10-14 days
manual work
1-2 days with automation
Workflow
PCB Design
Other EDA
RFPro EM
> 50 paths in 1 board
> 20 components in 1 path
Matching
Lumped optimization
PDK discrete optimization
Generate BOM
Lumped to PDK
Results | Total Time 1 RF Path | Total Time 50 RF Paths
Traditional workflow (manual) | 120 min | 6000 min (100 hrs)
Automated workflow | 15 min | 750 min (12.5 hrs)
Solution approach | Use automation to improve each Task within the Workflow | 
Results
8x
“Accelerate RF Board BOM Simulation with ADS Design Automation”, DAC ‘61
8x Speed-up per Freq band

## Slide 14: Use Case 3 (AI/ML Exploration)
How will industry incorporate AIML into everyday design?
IEEE Link
“Flexible Inverse Design of Microwave Filter Customized on Demand with Wavelet Transform Deep Learning”
IEEE Link
“A Design Methodology of MMIC Power Amplifiers Using AI-driven Design Techniques”
Examples of recent research
Engineering workflows are streamlined through Automation
APIs enable synthetic training data generation, even beyond T&M caapbility
Then, AI Models are developed, or AI Agents are integrated to manage.
DUT
Set up the tech files
Parameterize design
GENERATE
Setup sweeps
Run simulations
Post-process to FOM’s
TRAIN
Fit AI/ML models
Validate AI/ML models
DEPLOY
Metadata, versioning
Package/Encrypt model
Installer
AI Model Training Workflow
Filter Workflow w/ AI Agents
AI Optimizer
AI Agent
AI Agent
ACT
Assess Sensitivity
Generate Report
and compliance table
Yes
SYNTHESIZE
Synthesize filter
MEASURE
Set up schematic
Run Simulation
Generate/Update Layout
Run EM Simulation
DECIDE
Does the filter meet
Target spec?
No
Yes
Yes
OPTIMIZE
Change Parameters
Iterate
AI Agent
AI Agent
AI Agent
“State-of-the-Art: AI-Assisted Surrogate Modeling and Optimization for Microwave Filters”
IEEE Link
Published AI research
already
accumulating

## Slide 15: Use Case 3 (A/ML Exploration) : ML enabled by ADS APIs & scalability
Filpal (Malaysia) startup succeeds with ADS Python APIs
for AI-based Optimization research
https://www.youtube.com/watch?v=zVDZgyXg-6w
ANN for measurement-based PA workflow
(https://www.keysight.com/content/dam/keysight/en/vid/ungate/demos/ADS-Python-Automation-Applications.mp4)
17-page app note (new!)
Baylor University (US) succeeds with ADS Python APIs
for AI-based Loadpull research
https://www.youtube.com/watch?v=jvRouRay1jU
University of Chalmers automates machine learning
“Unthinkable Circuits”

## Slide 16: Re-imagining RF Design Using ADS Python APIs & AI/ML
Agenda
Python APIs in ADS
Case 1: Generative AI for Loadpull (Video from Baylor Univ, 11:00)
Case 2: “QR Code” Filters with RFPro (Video from Chalmers Univ, 9:00)
AI/ML Technologies in ADS

## Slide 17: Multidimensional Load-Pull Extrapolation Plugin for Accelerated Computer-Aided Design (CAD) Simulations in Keysight’s ADS
Jonathan E. Swindell1, Adam C. Goad1, Austin Egbert1, Casey Latham2, Matthew Ozalas2, Andy Howard2, Daren McClearnon2, Charles Baylis1, Robert J. Marks II1
1Baylor University
2Keysight Technologies
Jonathan_Swindell1@baylor.edu
PLAY VIDEO NEXT SLIDE

## Slide 19: ADS Python Success Story: Baylor University
“Multidimensional Load-Pull Extrapolation Plugin for Accelerated Computer-Aided Design (CAD) Simulations in Keysight’s ADS
Application Summary
Based on half-dozen observed Loadpull points…
Use AI image generation techniques to estimate the rest of the curved surface, draw contours, and quickly estimate what is possible with this device
How?
ADS is used to generate synthetic training data
130k Harmonic Balances of GaN device(s) vs. freq, bias, input power, and more
Conclusion
ADS 2025 APIs were essential and easy
AI can estimate points that are difficult/expensive to measure in real life and find solutions to multi-dimensional challenges
Keysight EDA Connect 2025

## Slide 20: Re-imagining RF Design Using ADS Python APIs & AI/ML
Agenda
Python APIs in ADS
Case 1: Generative AI for Loadpull (Video from Baylor Univ, 11:00)
Case 2: “QR Code” Filters with RFPro (Video from Chalmers Univ, 9:00)
AI/ML Technologies in ADS

## Slide 21: AI-Assisted Design of Microwave Circuits
Ludvig Fornstedt, Gabriel Melin, David Widén
Master’s Degree students,
Chalmers University of Technology, Sweden
PLAY VIDEO NEXT SLIDE
Keysight EDA Connect 2025

## Slide 23: ADS Python Success Story: Chalmers University
“AI-Assisted Design of Microwave Circuits”
Application Summary
Goal : find “Unthinkable Circuits” that humans would overlook or never consider
Use AI/ML techniques to do inverse design of microwave filters using pixelated layouts
How?
ADS used to generate synthetic training data
100k EM simulations vs. freq, raster metal patterns, trained a complex neural net
Genetic optimizer chooses closest response, using ANN to evaluate quickly
Conclusion
ADS 2025 APIs were essential and easy
Fast AI surrogate models with EM-level accuracy can transform design practices
Keysight EDA Connect 2025

## Slide 24: Re-imagining RF Design Using ADS Python APIs & AI/ML
Agenda
Python APIs in ADS
Case 1: Generative AI for Loadpull
Case 2: “QR Code” Filters with RFPro
AI/ML Technologies in ADS
    Artificial Neural Net modeling (ANN) Putting static data into motion
    ML Optimization Letting machines do the hard work
    Chatbots & Generative AI Intelligent assistants arrive in ADS

## Slide 25: Neural Nets – ANN’s can turn static data into executable models
From pictures on a datasheet…
…to nonlinear simulation!
Turn data into executable models
  Smoother, continuous interpolation from sparse, irregular, or multi-dimensional data
  Faster execution of behavioral mdoel
  Protects circuit and measurement IP
  Built into ADS 2025
General-purpose video tutorial series:
“Using AI to Create a Simulation Model” https://www.youtube.com/playlist?list=PLtq84kH8xZ9G8PkPdGMAAwxM1Y6dZ6oIC
  Part 1: https://www.youtube.com/watch?v=IYQ3b4YUQFM
  Part 2: https://www.youtube.com/watch?v=mWkHV1wfzFs
  Part 3: https://www.youtube.com/watch?v=ylrwYq5b_r8
Keysight EDA Connect 2025

## Slide 26: Neural Surrogates
Enabling modeling flexibility, 1000x acceleration for verification, and design re-use/twinning
Modeling Flexibility and measurement-based twins
20x-1000x faster for
Cross-domain verification
6G system-level and PHY Channel
Keysight EDA Connect 2025

## Slide 27: Let’s Apply ANNs to Loadpull PA Design – Problem Statement
Original Loadpull dataset.
How to use it?
Plot Contours
Pick the “Best” Complex Load
Finish the design in ADS
UNFORMATTED
RAW
MEASUREMENTS
1
2
3
Challenges:
“How to clean up the measured data?”  Python Automation
“How to turn the data into an executable model?”  ANNs
Keysight EDA Connect 2025

## Slide 28: Let’s Apply ANNs to Loadpull PA Design – Solution
Keysight EDA Connect 2025
ADS Datasets and Data Displays
ADS Models and Testbenches
IMPORT DATA
CLEAN IT UP
EXPORT IT
UNFORMATTED
RAW
MEASUREMENTS
https://docs.keysight.com/pages/viewpage.action?spaceKey=eesofkcads&title=Load+Pull+Data+GUI+for+ADS

## Slide 29: Let’s Apply ANNs to Loadpull PA Design – Solution
Keysight EDA Connect 2025
3 LEVEL OF ANN MODELS
UNFORMATTED
RAW
MEASUREMENTS
Data/Metadata Generation
Data / IP Storage
Filter/Clean Data
Algorithm & Training
AI/ML Verification
Watch now:
https://www.keysight.com/content/dam/keysight/en/vid/ungate/demos/Load-Pull-Modeling-with-Python-s-AI-Power.mp4

## Slide 30: OPTIONAL : Play Video Demo of Loadpull DataGUI (5:12) )

## Slide 31: For More Information on Loadpull and to download binaries
Application note & video on this Loadpull topic
  https://www.keysight.com/us/en/assets/3124-1550/application-notes/Measurement-Based-Artificial-Neural-Network-Simulation-Models-for-RF-Power-Amplifiers.pdf
  https://www.keysight.com/content/dam/keysight/en/vid/ungate/demos/Load-Pull-Modeling-with-Python-s-AI-Power.mp4
To access the ADS workspace and Python scripts from this Application Note, plus additional Jupyter Notebooks and schematic creation scripts:
  https://docs.keysight.com/display/eesofkcads/Measurement-based+Artificial+Neural+Network+Simulation+Models+for+RF+Power+Amplifiers (Keysight Knowledge Center)
To download a Python based add-on for ADS which reads measured load pull data and generates models similar to the ones described in this work:
  https://docs.keysight.com/display/eesofkcads/Load+Pull+Data+GUI+for+ADS (Keysight Knowledge Center)
Keysight EDA Connect 2025

## Slide 32: Re-imagining RF Design Using ADS Python APIs & AI/ML
Agenda
Python APIs in ADS
Case 1: Generative AI for Loadpull
Case 2: “QR Code” Filters with RFPro
AI/ML Technologies in ADS
    Artificial Neural Net modeling (ANN) Putting static data into motion
    ML Optimization Letting machines do the hard work
    Chatbots & Generative AI Intelligent assistants arrive in ADS

## Slide 33: ML Optimization – a new generation of algorithms
Dynamic Gaussian distribution adjusts its search area by learning from the data, giving oval shaped predictions
Breakthrough techniques unlock a proven concept
Challenge
Conventional optimizers struggle when handling more than 20 variables and/or objectives/goals
Result: Users need to work around limitations.  Manually break into many smaller problems
Older fixed Gaussian distributions try within a circle of predictions
AI/ML approaches are smart and adaptive, supporting higher optimization dimensions
Solution
Use new AI/ML-driven optimization techniques:
Expanded capacity to handle 40+ parameters, multi-objectives
Able to automate complex processes, accelerating workflow
Notes: Optimization is at the core of many of our products, but traditional methods face significant limitations:
Most conventional optimizers struggle when handling more than 20 parameters, leading to inefficiencies.
As a result, customers need to manually break down large-scale problems into smaller, more manageable ones.
To overcome these challenges, our team leveraged AI/ML-driven optimization techniques:
Expanded the optimization capacity to handle 40+ parameters seamlessly.
Automated complex processes, significantly reducing the workload for customers

## Slide 34: ML Optimization – a new generation of algorithms
Abilities of Modern Optimizers:
  Large number of input Variables, and output Goals
  Fewer iterations needed to converge, given complex problems
Optimizers especially shine when:
  There is no historical data –– cannot apply supervised/unsupervised Machine Learning algorithms
  Limited number of iterations (less than 10K) –– cannot apply Reinforcement learning
Recently developed optimization algorithms:
  CMA-ES, LSHADE, LSHADE-SPACMA, TSA, TuRBO
  Particle Swarm, Corana Simulated Annealing, Non Dominated Sorted Genetic Algorithm II (NSGA-II), more
  Ability to integrate your own optimizer from PyTorch, Pymoo, etc
IC-CAP 2025 ML Optimizer
< 10 Parameters
40 + Parameters
with ML
Zijian Song et al.,
“Automating Compact Model Parameter Extraction: Industry-Grade Implementation and Benchmarking of Machine Learning-Driven Derivative-Free Algorithms”, 2024 IEEE NAFEMS
Keysight EDA Connect 2025
ADS 2024 Worst-Case Bit-Pattern Generator for Eye Diagram
14x Simulation Speed Up
Majid Ahadi Dolatsara,
“Worst-Case Bit-Pattern Generator for Eye Diagram Analysis of Non-LTI High-Speed Channels”, 2024 Signal Integrity Journal
Graphics credit: Wikipedia
Notes: Traditional optimization of multi-objective goals combines all goals into single error function with weights assigned to each objective based on human assumption of their relative importance. These assumptions are made before the optimization begins and does not produce the optimal combinations of multi-objective goals called the Pareto front which shows the trade offs amongst the competing goals. These new optimization techniques address these limitations to enable multi-objectives (e.g., EVM, Stability, Efficiency, Temperature and Size) goals with large number of input variables (i.e., high dimensional search space) to be optimized across simulation domains and design hierarchies.

## Slide 35: ML Optimization results : Adjusting 27 Parameters in ICCAP
Improved workflow for complex task
Analyzed and compared simulated vs. measured GaN-on-SiC HEMT characteristics
  CMA-ES achieved the best fitting performance
  L-BFGS-B and LM results overlapped due to similar fitting performances
Implication for RF Circuit design:
  faster Optimizer convergence is coming soon on realistic circuits with many parameters
Keysight EDA Connect 2025

## Slide 36: ML Optimization – Applied to Complex Verifications
Bayesian Optimization toward a maximal aggressor waveform
  Finds the worst-case Eye Diagram, using << shorter bit sequence, in the fewest # of Transient search simulations
  Result: Dramatic simulation speed-ups with optimized waveform
Bayesian optimizer now added to ADS
Bayesian optimization for the Equalizers to clean up Eye Closure
Worst-case Eye Pattern for HSD/Signal Integrity applications
?
Same Eye Closure
But now 47x Faster
 | Eye height (mV) | Eye width (ps) | Number of bits
Worst-eye | 639 | 745 | 5,760
Transient Eye | 639 | 744 | 1,000,000
Keysight EDA Connect 2025
Notes: A Bayesian optimization algorithm was used to seek the bit pattern that caused the worst-case Eye Closure
If you used a regular Transient simulation with a typical optimizer, it would take a great number of simulations to find a worst case, and each of those cases would take a long time to simulate
This produces a shorter sequence that exposes the same freqeuency dependence and waveform statistics, but all analyses based on this shorter sequence will now be much faster.
Reference: M. Ahadi, et. al. “Worst-case eye analysis of high-speed channels based on Bayesian optimization”, IEEE TEMC, V. 63. N. 1, 2020. (Best TEMC Transaction Award)

## Slide 37: Re-imagining RF Design Using ADS Python APIs & AI/ML
Agenda
Python APIs in ADS
Case 1: Generative AI for Loadpull
Case 2: “QR Code” Filters with RFPro
AI/ML Technologies in ADS
    Artificial Neural Net modeling (ANN) Putting static data into motion
    ML Optimization Letting machines do the hard work
    Chatbots & Generative AI Intelligent assistants arrive in ADS

## Slide 38: Introducing Keysight’s EDA Chat
1000’s of pages of Documentation and KC documents at your fingertips
NEW ADS USER
Ask chat question
EDA CHATBOT Learned best tricks from 100s of Keysight Experts,
Documents, resources
NEW ADS USER
Faster success
on real design tasks
Benefits
Natural language responses
Hyperlinks to original ADS Doc & KC references
Avoids obsolete and conflicting product info
ADS only : Not a general engineering reference or design agent
Productivity
New users: onboard quickly with ADS
Experienced users: find detailed references easily
Keysight EDA Connect 2025
Succeed faster, beginning with ADS 2025 Update 2
Notes: Keysight EDA proprietary enhancements to data
ADS documentation
API docs & release notes
ADS Error Messages and Warnings
KC Articles > 80 hits
YouTube tutorials since 2020
Experts hand-contributed data
App notes and PPTs
Keep track of Versioning
Hyperlinks to original references
Voluntary user-submitted feedback

## Slide 39: Keysight EDA Chat – demo preview
Notes: Keysight EDA Chat client – unreleased version Nov 2024

## Slide 40: Re-imagining RF Design Using ADS Python APIs & AI/ML
Conclusion
Python APIs in ADS
Case 1: Generative AI for Loadpull (Video from Baylor Univ)
Case 2: “QR Code” Filters with RFPro (Video from Chalmers Univ)
AI/ML Technologies in ADS
Conclusion

## Slide 41: Conclusion
You can achieve more through Automation
  Python is an easy, universal language, and ADS APIs make automation easier than ever.
  Multiple interfaces : Command line inside ADS, headless from outside, or custom Apps
  Microsoft VS Code and Copilot are remarkably helpful
  Anyone can do it!
Automation is the on-ramp to AI/ML
  A new wave of technology is coming to assist designers
  Designers who use AI will out-produce Designers who don’t
  Invest now to enhance your skills
Open, standards-based workflows
  AI technology is moving quickly. Open standards reduce risk.
  Keysight is working toward Open, Secure, and Scalable workflows

## Slide 42: Learn more about ADS APIs & Python Automation
Baylor University (US) succeeds with ADS Python APIs
for AI-based Loadpull research
https://www.youtube.com/watch?v=jvRouRay1jU
Filpal (Malaysia) startup succeeds with ADS Python APIs
for AI-based Optimization research
https://www.youtube.com/watch?v=zVDZgyXg-6w
ANN for measurement-based PA workflow
(Video coming soon)
17-page app note (new!)
Whitepaper outlining what’s possible with ADS python
Direct link

## Slide 43: Learn more about ADS APIs & Python Automation
Python Tutorials and resources
ADS 2025 U1 Python API documentation
  https://docs.keysight.com/ads2025update1/ads-python-api-documentation
ADS Python Getting Started (resource page)
  https://docs.keysight.com/display/eesofkcads/ADS+Good+Reference+Starts+for+AEL+and+Python+Scripting+or+Command+Line
To learn more about PathWave Data Tools Python Library (v. 0.11.0):
  https://docs.keysight.com/pwdt0x11x0 (keysight.com)
To learn more about Python automation in Keysight Advanced Design System:
  Python APIs for EDA Workflows (keysight.com)
To learn about Keysight EDA Chat
  https://docs.keysight.com/display/keysightedachat/About+Keysight+EDA+Chat
Keysight EDA Connect 2025

## Slide 44
Questions?

## Slide 46: Re-imagining RF Design Using ADS Python APIs & AI/ML
Agenda
Python APIs in ADS
Case 1: Generative AI for Loadpull (Video from Baylor Univ)
Case 2: “QR Code” Filters with RFPro (Video from Chalmers Univ)
AI/ML Technologies in ADS

## Slide 47: Multidimensional Load-Pull Extrapolation Plugin for Accelerated Computer-Aided Design (CAD) Simulations in Keysight’s ADS
Jonathan E. Swindell1, Adam C. Goad1, Austin Egbert1, Casey Latham2, Matthew Ozalas2, Andy Howard2, Daren McClearnon2, Charles Baylis1, Robert J. Marks II1
1Baylor University
2Keysight Technologies
Jonathan_Swindell1@baylor.edu
PLAY VIDEO

## Slide 48: Outline
Motivation
WGAN Smith Tube Image Completion
Model Architecture
Error Metrics
AI-powered Accelerated Computer-Aided Design via ADS Plugin
Results
Next Steps and Conclusions

## Slide 49: Nonlinear Power Amplifier Design
Traditional RF Design
AI-Powered RF Design and Automation
Power Sweep
Load-Pull
Bias Sweeps
Requires many measurements and many design iterations
Requires years of domain expertise to complete many RF designs
Requires slow acquisition and expensive specialty equipment for measurements at high frequencies and high powers
Bias Sweeps
Load-Pull
Power Sweep
AI-powered image completion enables a reduction in the number of required simulations or measurements.
AI-powered design and automation tools enable less experience to be required to complete an RF design.
AI-powered RF tools can accelerate measurements and simulation actions required by many applications.

## Slide 50: Partial Load-Pull Extrapolation
Deep learning image completion methods can be leveraged to extrapolate an entire set of load-pull performance contours from a small set of measured impedances
Image Completion
[1] A. Egbert, C. Baylis and R. J. Marks, "Extrapolation of Load-Pull Data: A Novel Use of GAN Artificial Intelligence Image Completion," in IEEE Trans. Microw. Theory Techn., vol. 70, no. 11, pp. 4849-4856, Nov. 2022, doi: 10.1109/TMTT.2022.3209700.
Notes: To apply this as an image completion problem and apply AI, we need to represent load-pull contours as an image.

## Slide 51: Smith Chart Data as Grayscale Image
Output power contours as gray scale pixel values

## Slide 52: Smith Tube Data as an Image in 3 Dimensions
Top Slice
Bottom Slice
…
[2] J. E. Swindell, A. C. Goad, A. Egbert, C. Baylis, R. J. Marks, “Multidimensional Load-Pull Extrapolation using Generative Adversarial Networks” in IEEE MTT-S Latin America Microwave Conference, San Juan, Puerto Rico, Jan. 2025.

## Slide 53: Generative Adversarial Networks (GAN) Image Completion
Two neural networks trained iteratively
Generator: provides reliable datasets meeting certain requirements
Discriminator (Critic): trained to recognize datasets meeting requirements.
Wasserstein GAN was used in initial work
GAN Construction:
Image Completion Search Process:
Notes: Transition MLAI methods require lots of training data.

## Slide 54: Data Collection
Variable | Start | End | Steps
ZLoad | 476 radially distributed points in the Smith Chart |  | 560
ZSource | Select Points with ¦Γ¦ < 1 -1 < Γr < 1 -1 < Γi < 1 |  | 69
Gate Voltage | -2V | 0V | 11
Drain Voltage | 0.1V | 6V | 11
Power In | -10dBm | 15 dBm | 28
Frequency | 3.00 GHz | 3.00 GHz | 1
Modelithics MWT-1 Nonlinear Device Transistor Model:
ADS Simulation: Variable Sweeps:
Training data collected using ADS 2024 Update 2 with custom Python scripts used to enable data collection parallelization across two desktop computers.
Completed 130,912,320 simulations in ~21 hours.
ADS Python API Enables:
Programmatic design of schematics and layouts
Run simulations with changing variables
Easy access and integration with other systems
Notes: After collecting and processing the data we need to train the model. If you interested in the preprocessing steps check out our paper on this work.

## Slide 55: Model Training and Compute Resources
Compute Resources:
  CPU: AMD Ryzen 5800X3D
  RAM: 32 GB DDR4
  GPU: NVIDIA RTX 4070Ti Super (16GB VRAM)
Training Time: 3.25 minutes per 30k images per epoch
Image credit: Igorslab.de:
https://www.igorslab.de/en/pny-geforce-rtx-4070-ti-super-xlr8-gaming-verto-epic-x-16-gb-review-more-clock-speed-through-better-cooling/4/
Notes: Uses 30k images and 50 epochs for results here. Unclear if >30k images may be required for better generality

## Slide 56: Types of Error Metrics
Distance Metrics
Distance between the position of the true optimum value on a contour and the predicted position of that true optimum.
Value Metrics
The difference between the value predicted at a contour position and the true value at that contour position.

## Slide 57: Distance Error Metrics
Slice Distance: distance between predicted and true optimum location on a single power slice in units of pixels
Solid Distance: distance between predicted and measured optimum location on the Smith Tube in units of voxels

## Slide 58: Value Error Metrics
Peak Level Error: the difference between the maximum output power at the measured optimum location in the Smith Tube of the measured and predicted images in units of dB
Opportunity Error: the difference between the measured behavior at the measured and predicted optimum locations in units of dB
Expectation Error: the difference between the measured and predicted performance at the predicted optimum in units of dB

## Slide 59: Results
Table I: Measurement Extrapolation Error
Error Metric | Mean | Median
Slice Distance (Reflection Coefficient) | 0.147 | 0.129
Solid Distance (voxels) | 2.028 | 1.414
Peak Level Error (dB) | -0.1524 | -0.1435
Opportunity Error (dB) | 0.1883 | 0.06501
Expectation Error (dB) | -0.3407 | -0.277
This accuracy was achieved with a 1,500 times reduction in the required number of simulated load-pull points!
[2] J. E. Swindell, A. C. Goad, A. Egbert, C. Baylis, R. J. Marks, “Multidimensional Load-Pull Extrapolation using Generative Adversarial Networks” in IEEE MTT-S Latin America Microwave Conference, San Juan, Puerto Rico, Jan. 2025.
Notes: Add conversion!

## Slide 60: Multidimensional Load Pull Extrapolation on Measured Data
Extrapolating from 16 points measured on the MWT 1 Transistor can complete a Smith Tube with comparable errors to the simulation case.
This method can be used to enable a 1,500 - times reduction in requirement load-pull measurement!
[3] [Submitted] J. E. Swindell, A. C. Goad, A. Egbert, Et. al., “Measurement Validation of AI-Powered Multidimensional Nonlinear Load-Pull Extrapolation ”, IEEE International Microwave Symposium, San, Francisco CA, 2025.

## Slide 61: Comparison between Simulation and Measured Results
Table 2. Measurement Extrapolation Error
Table 1. Simulation Extrapolation Error
Error Metric | Mean | Median
Slice Distance (Reflection Coefficient) | 1.907 | 1.414
Solid Distance (voxels) | 2.402 | 2.236
Peak Level Error (dB) | -0.7133 | -0.5935
Opportunity Error (dB) | 0.2595 | 0.1657
Expectation Error (dB) | -0.9728 | -0.7984
Error Metric | Mean | Median
Slice Distance (Reflection Coefficient) | 2.271 | 2.000
Solid Distance (voxels) | 2.028 | 1.414
Peak Level Error (dB) | -0.1524 | -0.1435
Opportunity Error (dB) | 0.1883 | 0.06501
Expectation Error (dB) | -0.3407 | -0.277

## Slide 62: AIML can Accelerate Computer-Aided Design
These results are awesome, but remember our frustrated engineer:
to make use of these AIML advancements, we need to deploy these tools in RF CAD software.
AIML-powered RF circuit design and optimization requires CAD tools with APIs that enable design automation. Baylor has used Keysight ADS’s Python Integration API to develop an ADS plugin that can reduce the required number of load-pull simulations by 1500 times.

## Slide 63: AI-powered accelerated Computer-Aided Design via RF Design Automation
*Video removed processing time. Ported MATLAB processing to Python which is currently unoptimized.

## Slide 65: Applications

## Slide 66: High-Power, High-Frequency Load Pull Approximation
While active load-pull measurement devices can take load-pull measurements quickly, these devices are expensive and may not be available for high-power or high-frequency devices.
In these cases, multidimensional load-pull extrapolation can approximate performance at those locations.
Not available for very high-power or high-frequency applications
Notes: The active load pull device shown is the S94573B Wideband Active Load Pull Export Control from Keysight.

## Slide 67: Accelerated Simulations can speed up large scale simulations
Multidimensional Load-Pull extrapolation can be used to accelerate large-scale simulations.
Measurements or simulations can be taken at strategic points in the search space and then passed to the ML network for extrapolation.
This accuracy was achieved with a 1,500 times reduction in the required number of simulated load-pull points!

## Slide 68: Accelerated Measurements Enable Real-Time Reconfiguration

## Slide 70: Re-imagining RF Design Using ADS Python APIs & AI/ML
Agenda
Python APIs in ADS
Case 1: Generative AI for Loadpull (Video from Baylor Univ)
Case 2: “QR Code” Filters with RFPro (Video from Chalmers Univ)
AI/ML Technologies in ADS

## Slide 71: AI-Assisted Design of Microwave Circuits
Ludvig Fornstedt, Gabriel Melin, David Widén
Master’s Degree students,
Chalmers University of Technology, Sweden
PLAY VIDEO

## Slide 72: Who are we?
Master's Students at Chalmers University of Technology, Sweden:
  Ludvig Fornstedt – Complex Adaptive Systems Program
  Gabriel Melin – Complex Adaptive Systems Program
  David Widén – Wireless, Photonics, and Space Engineering Program
Worked on AI-Assisted Design of Microwave Circuits as part of our Bachelor's Thesis.

## Slide 73: AI-Assisted Design for "QR-code" filters
Quick and opens up new, previously unthinkable design solutions.

## Slide 74: Overview
Simulate
~100 000 Circuits
in ADS
Train a CNN
to predict
s-parameters
Use the CNN in a
Genetic Algorithm
to produce circuit

## Slide 75: Simulation
Represent circuit as a binary matrix
  1=metal
  0= no metal
Each square is 0.9 mm in length
  L ≈ 120° @ 5 GHz
Randomly generate and select 13 x 13 matricies which satisfy certain conditions

## Slide 76: Simulation
Convert binary matrices into layouts in ADS using python
Simulate S-parameters for 19 points between 1-10 GHz
Notes: Convert the generated matricies to circuits in ads. All that is needed is setting up the substrate and simulation setting in ADS and then the rest can be done without opening ADS.
We simulated the circuit between 1 and 10 GHz
We simulate 100 000 circuits which takes us about 4s

## Slide 77: Simulation
Re(S11)
Im(S11)
Re(S21)
Im(S21)
Re(S22)
Im(S22)
. . . (for 19 frequencies)
Start simulation and extract data using python
Process all data using python
Notes: We can then automatically extract the data from ADS back to python for post processing.

## Slide 78: Neural-Network
Re(S11)
Im(S11)
Re(S21)
Im(S21)
Re(S22)
Im(S22)
. . . (for 19 frequencies)
14 convolutional layers with residual connections
5 fully connected layers

## Slide 79: Neural-Network

## Slide 80: Genetic Optimization
Initial population
Selection
Crossover
Mutation
Evaluating
population
with NN
Solution
One generation
Evaluation:
Using the NN to predict the S-parameters
Compare them to the chosen goal parameters
Calculating a fitness score for each individual

## Slide 81: Results

## Slide 82: Results
Time requirements:
  Simulate 100 000 circuits ≈ 111 hours
  Train CNN ≈ 8 hours
  Generate one circuit ≈ 50 min

## Slide 83: Lowpass filter
Design Goals:
|S21| =1 (f ≤ 7 GHz)
S21=0 (f > 7 GHz)
ADS MoM MW
Measurement
FEM (3rd party)

## Slide 84: Bandpass filter
Design Goals:
|S21| =1 (3.5 ≤ f ≤ 6.5 GHz)
S21=0 (otherwise)
ADS MoM MW
Measurement
FEM (3rd party)

## Slide 85: Thank you for listening!
Ludvig Fornstedt, Gabriel Melin, David Widén